WSN simulator
A Wireless Sensor Network simulator in Python and C++ (via SWIG).
It basically simulates the communication among nodes and communication with the base station. It has a energy model that helps estimates the network lifetime. It has some pre-defined scenarios (including clustering techniques):
- Direct Communication (from nodes directly to the base station);
- MTE (M. Ettus. System Capacity, Latency, and Power Consumption in Multihop-routed SS-CDMA Wireless Networks. In Radio and Wireless Conference (RAWCON 98), pages 55–58, Aug. 1998)
- LEACH (W. Heinzelman, A. Chandrakasan, and H. Balakrishnan, Energy-efficient communication protocols for wireless sensor networks, In Proceedings of the 33rd Annual Hawaii International Conference on System Sciences (HICSS), Hawaii, USA, January 2000.)
- FCM (D. C. Hoang, R. Kumar and S. K. Panda, "Fuzzy C-Means clustering protocol for Wireless Sensor Networks," 2010 IEEE International Symposium on Industrial Electronics, Bari, 2010, pp. 3477-3482.)
It also implements a modified version of PSO (Particle Swarm Optimization) in order to schedule sleeping slots to every node at every communication round. This implementation is based on (C. Yu, W. Guo and G. Chen, "Energy-balanced Sleep Scheduling Based on Particle Swarm Optimization in Wireless Sensor Network," 2012 IEEE 26th International Parallel and Distributed Processing Symposium Workshops & PhD Forum, Shanghai, 2012, pp. 1249-1255.), but contains improvements, specially concerning the learning of better solutions.
# Running it
1 - Choose your settings in the configuration file (config.py)
2 - python setup.py build_ext --inplace
3 - python run.py
# Requirements
All non-trivial requirements (the ones you cannot get via pip install) are inside this repository. Trivial requirements include:
- matplotlib for plotting graphics
- numpy for array manipulation and operations
- logging for improved printing (warnings, errors, running information)
- inspect (for debugging)
- multiprocessing (disabled) for reducing simulation time

# Code structure
Code is structured as follows:
- /python contains all python modules and classes
  - /python/network/ contains classes that model the energy source, the network, each node and the aggregation models
    - energy_source.py models battery and “plugged in” sources.
    - network.py models the network, which is basically a list of nodes.
    - node.py represent every node in the network and contains an energy source.
    - aggregation_model.py offers different aggregations models (from zero cost to total cost).
  - /python/routing/ contains classes that model all routing protocols: fcm, mte, leach and direct communication. It also contains code for running Dijkstra’s path (used in MTE) and a file named prioridict.py that is also used for MTE. The file routing_protocol.py contains a class that is extended by all routing protocols and that define a common interface for these protocols (this way the network code that uses these protocols can be generic and not different for each protocol).
    - dijkstra.py implements Dijkstra’s path.
    - direct_communication.py implements DC.
    - fcm.py implements FCM protocol.
    - mte.py implements MTE protocol.
    - peach.py implements LEACH protocol.
    - prioridict.py is used by dijkstra.py to describe the cost graph.
    - routing_protocol.py is an interface to all routing protocols.
  - /python/sleep_scheduler/ contains a single class that represents an interface to sleep scheduling protocols. It wrapps the algorithms implemented in C++.
    - sleep_scheduler.py is the wrapper that holds c++ sleep scheduling objects.
  - /python/utils contains the files grid.py, region.py and regions_converter.py that are used for modeling and calculating the coverage and overlapping areas.
    - Grid.py represents the grid over the field.
    - region.py represents a single region with its owners.
    - regions_converter.py reads the network and convert it to regions.
    - tracer.py stores the traces that are plotted or saved.
    - utils.py contains all plot functions plus other utility functions.
- /cc contains all c++ classes and swig interfaces.
  - Ecca.h, ecca.cc, ecca.i: ECCA header, implementation and swing interface.
  - modified_pso.h, modified_pso.cc, modified_pso.i: Modified PSO header, implementation and swing interface.
  - pso.h, pso.cc, pso.i: PSO header, implementation and swing interface.
  - genetic_algorithm.h, genetic_algorithm.cc, genetic_algorithm.i: Genetic algorithm header, implementation and swing interface.
  - Regions.h, regions.cc: stores the regions
  - individual.h, individual.cc: represent and individual in the genetic algorithm
  - optimizer.h, optimizer.cc, optimizer.i: represent an optimizer. PSO, ECCA, Genetic algorithm and Modified PSO inherit from this class.
  - types.h and custom_types declares some custom types.
- /scripts contain a single python script to plot energy graphs
- /results will be generated when run.py is called and simulation results will be stored there

config.py has no executable code and contains all configurations. It also contains a list called scenarios that stores all scenarios that are going to be simulated. It can also contain executable code to change parameters during the simulation without requiring any user interference. This file is documented and contains examples of use.
Run.py has two functions: run_scenarios that run all scenarios specified at config.py and run_parameter_sweep that perform and example of code that runs the same scenarios but with different paramenters.
Each file is commented and it describes its behavior.